## Slide 1: EIE 411 Computer Organization and Architecture
MODULE 04 A: STORAGE & INPUT/OUTPUT SYSTEM
Part C: Computer Organization & Assembly Programming
&
Assembly Language Programming
LECTURER: ENGR. KENNEDY OKOKPUJIE

## Slide 2: Revision of Interrupts
Interrupt is a process where an external device can get the attention of the microprocessor. The process starts from the I/O device. The process is asynchronous.
Interrupts can be classified into two types:
Maskable (can be delayed)
Non-Maskable (cannot be delayed)

## Slide 3: Revision of Interrupts
Interrupts can also be classified into:
Vectored (the address of the service routine is hard-wired)
Non-vectored (the address of the service routine needs to be supplied externally)
An interrupt is considered to be an emergency signal. The Microprocessor should respond to it as soon as possible. When the Microprocessor receives an interrupt signal, it suspends the currently executing program and jumps to an Interrupt Service Routine (ISR) to respond to the incoming interrupt. Each interrupt will most probably have its own ISR.

## Slide 4: Responding to Interrupts
Responding to an interrupt may be immediate or delayed depending on whether the interrupt is maskable or non-maskable and whether interrupts are being masked or not.
There are two ways of redirecting the execution to the ISR depending on whether the interrupt is vectored or non-vectored. The vector is already known to the Microprocessor. For non-vectored interrupts, the device will have to supply the vector to the Microprocessor

## Slide 5: Revision of Computer Bus Structure
Representation of SERIAL transmission of data. Obviously, only one wire is required for serial transmission, the bits of information being sent down the line consecutively.
Serial data transmission

## Slide 6: Revision of Computer Bus Structure
An alternative method of conveying digital information is by PARALLEL transmission. Here several wires are used so that an equivalent number of bits of information can be transmitted simultaneously as shown.
Parallel transmission

## Slide 7: Revision of Computer Bus Structure
DATA BUS
Processed information i.e. data, data memory is determined by the amount of data a microprocessor processes at once i.e. the no of bit it processed once.
A group of 8 bits is called “Byte”
A group of 4 bits is called “Nibble”

## Slide 8: Revision of Computer Bus Structure
For example
A 64KB microprocessor.
64K means that the microprocessor has 64 memory location i.e. Address locations
The byte (B) means that each of the 64 memory location can process 8 bits once

## Slide 9: Revision of Computer Bus Structure
CONTROL BUS/LOGIC
This generates control signals and coordinates all the activities to make sure operations are done normally by sending information or signal through the control bus.
Every processor comes with a crystal oscillator i.e. a signal built on a crystal.

## Slide 10: Revision of Computer Bus Structure
Signal generators Limitations are
Unstable at high frequency except crystal oscillator. This oscillator generate stable high frequency signals
Clock signals used by the control logic to coordinates its activities. Since the frequency is inversely proportional to the period, we talk about frequency in microprocessor.

## Slide 11: Revision of Computer Bus Structure
Address Bus gives the memory capacity of the processor.
The maximum no of address is given as 2n
where n is the no of bits.
216 = 210 X 216 = 26 X 1K = 64K

## Slide 12: NOTE
Programming a memory chip mean to store information or data into it.

## Slide 13: Focus
Assembly-, Machine-, and High-Level Languages
Assembly Language Programming Tools
Programmer’s View of a Computer System
Basic Computer Organization

## Slide 14: A HIERARCHY OF LANGUAGES

## Slide 15: ASSEMBLY AND MACHINE LANGUAGE
Machine language
  Native to a processor: executed directly by hardware
  Instructions consist of binary code: 1s and 0s
Assembly language
  A programming language that uses symbolic names to represent operations, registers and memory locations.
  Slightly higher-level language
  Readability of instructions is better than machine language
  One-to-one correspondence with machine language instructions
Assemblers translate assembly to machine code
Compilers translate high-level programs to machine code
  Either directly, or
  Indirectly via an assembler

## Slide 16: COMPILER AND ASSEMBLER

## Slide 17: INSTRUCTIONS AND MACHINE LANGUAGE
Each command of a program is called an instruction (it instructs the computer what to do).
Computers only deal with binary data, hence the instructions must be in binary format (0s and 1s) .
The set of all instructions (in binary form) makes up the computer's machine language. This is also referred to as the instruction set.

## Slide 18: INSTRUCTION FIELDS
Machine language instructions usually are made up of several fields. Each field specifies different information for the computer. The major two fields are:
Opcode field which stands for operation code and it specifies the particular operation that is to be performed.
  Each operation has its unique opcode.
Operands fields which specify where to get the source and destination operands for the operation specified by the opcode.
  The source/destination of operands can be a constant, the memory or one of the general-purpose registers.

## Slide 19: ASSEMBLY VS. MACHINE CODE

## Slide 20: TRANSLATING LANGUAGES
English: D is assigned the sum of A times B plus 10.
High-Level Language: D = A * B + 10
Intel Assembly Language:
mov eax, A
mul B
add eax, 10
mov D, eax
Intel Machine Language:
A1 00404000
F7 25 00404004
83 C0 0A
A3 00404008
A statement in a high-level language is translated typically into several machine-level instructions

## Slide 21: MAPPING BETWEEN ASSEMBLY LANGUAGE AND HLL
Translating HLL programs to machine language programs is not a one-to-one mapping
A HLL instruction (usually called a statement) will be translated to one or more machine language instructions

## Slide 22: ADVANTAGES OF HIGH-LEVEL LANGUAGES
Program development is faster
  High-level statements: fewer instructions to code
Program maintenance is easier
  For the same above reasons
Programs are portable
  Contain few machine-dependent details
    Can be used with little or no modifications on different machines
  Compiler translates to the target machine language
  However, Assembly language programs are not portable

## Slide 23: WHY ASSEMBLY LANGUAGE?
Accessibility to system hardware
  Assembly Language is useful for implementing system software
  Also useful for small embedded system applications
Space and Time efficiency
  Understanding sources of program inefficiency
  Tuning program performance
  Writing compact code
Writing assembly programs gives the computer designer the needed deep understanding of the instruction set and how to design one
To be able to write compilers for HLLs, we need to be expert with the machine language. Assembly programming provides this experience

## Slide 24: ASSEMBLY VS. HIGH-LEVEL LANGUAGES

## Slide 25: ASSEMBLER
Software tools are needed for editing, assembling, linking, and debugging assembly language programs
An assembler is a program that converts source-code programs written in assembly language into object files in machine language
Popular assemblers have emerged over the years for the Intel family of processors. These include …
  TASM (Turbo Assembler from Borland)
  NASM (Netwide Assembler for both Windows and Linux), and
  GNU assembler distributed by the free software foundation

## Slide 26: LINKER AND LINK LIBRARIES
You need a linker program to produce executable files
It combines your program's object file created by the assembler with other object files and link libraries, and produces a single executable program
LINK32.EXE is the linker program provided with the MASM distribution for linking 32-bit programs
We will also use a link library for input and output
Called Irvine32.lib developed by Kip Irvine
  Works in Win32 console mode under MS-Windows

## Slide 27: ASSEMBLE AND LINK PROCESS
A project may consist of multiple source files
Assembler translates each source file separately into an object file
Linker links all object files together with link libraries
Source
File
Source
File
Source
File
Assembler
Object
File
Assembler
Object
File
Assembler
Object
File
Linker
Executable
File
Link
Libraries

## Slide 28: DEBUGGER
Allows you to trace the execution of a program
Allows you to view code, memory, registers, etc.
Example: 32-bit Windows debugger

## Slide 29: EDITOR
Allows you to create assembly language source files
Some editors provide syntax highlighting features and can be customized as a programming environment

## Slide 30: PROGRAMMER’S VIEW OF A COMPUTER SYSTEM
Application Programs
High-Level Language
Assembly Language
Operating System
Instruction Set
Architecture
Microarchitecture
Digital Logic
Level 0
Level 1
Level 2
Level 3
Level 4
Level 5
Each level hides the details of the level below it
Increased level of abstraction

## Slide 31: PROGRAMMER'S VIEW
Application Programs (Level 5)
  Written in high-level programming languages
  Such as Java, C++, Pascal, Visual Basic . . .
  Programs compile into assembly language level (Level 4)
Assembly Language (Level 4)
  Instruction mnemonics are used
  Have one-to-one correspondence to machine language
  Calls functions written at the operating system level (Level 3)
  Programs are translated into machine language (Level 2)
Operating System (Level 3)
  Provides services to level 4 and 5 programs
  Translated to run at the machine instruction level (Level 2)

## Slide 32: PROGRAMMER'S VIEW
Instruction Set Architecture (Level 2)
  Specifies how a processor functions
  Machine instructions, registers, and memory are exposed
  Machine language is executed by Level 1 (microarchitecture)
Microarchitecture (Level 1)
  Controls the execution of machine instructions (Level 2)
  Implemented by digital logic (Level 0)
Digital Logic (Level 0)
  Implements the microarchitecture
  Uses digital logic gates
  Logic gates are implemented using transistors

## Slide 33: INSTRUCTION SET ARCHITECTURE (ISA)
Collection of assembly/machine instruction set of the machine
Machine resources that can be managed with these instructions
  Memory
  Programmer-accessible registers.
Provides a hardware/software interface

## Slide 34: INSTRUCTION SET ARCHITECTURE (ISA)

## Slide 35: CPU MEMORY INTERFACE
Address Bus
  Memory address is put on address bus
  If memory address = m bits then 2m locations are addressed
Data Bus: b-bit bi-directional bus
  Data can be transferred in both directions on the data bus
  Note that b is not necessary equal to w or s. So data transfers might take more than a single cycle (if w > b) .
Control Bus
  Signals control
  transfer of data
  Read request
  Write request
  Complete transfer

## Slide 36: CPU MEMORY INTERFACE

## Slide 37: MEMORY DEVICES
ROM (Read-Only-Memory)
  A read-only-memory, non-volatile i.e. stores information permanently
  Has random access of stored information
  Used to store the information required to startup the computer
  Many types: ROM, EPROM, EEPROM, and FLASH
  FLASH memory can be erased electrically in blocks
Cache
  A very fast type of RAM that is used to store information that is most frequently or recently used by the computer
  Recent computers have 2-levels of cache; the first level is faster but smaller in size (usually called internal cache), and the second level is slower but larger in size (external cache).

## Slide 38: The Need for a Memory Hierarchy
Widening (expand) speed gap between CPU and main memory
  Processor operation takes less than 1 ns
  Main memory requires more than 50 ns to access
Each instruction involves at least one memory access
  One memory access to fetch the instruction
  Additional memory accesses for instructions involving memory data access
Memory bandwidth limits the instruction execution rate
Cache memory can help bridge the CPU-memory gap
Cache memory is small in size but fast

## Slide 39: PROCESSOR-MEMORY PERFORMANCE GAP
CPU: 55% per year
DRAM: 7% per year
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
1982
Processor-Memory
Performance Gap: (grows 50% per year)
Performance
“Moore’s Law”
1980 – No cache in microprocessor
1995 – Two-level cache on microprocessor

## Slide 40: Typical Memory Hierarchy
Registers are at the top of the hierarchy
  Typical size < 1 KB
  Access time < 0.5 ns
Level 1 Cache (8 – 64 KB)
  Access time: 0.5 – 1 ns
L2 Cache (512KB – 8MB)
  Access time: 2 – 10 ns
Main Memory (1 – 2 GB)
  Access time: 50 – 70 ns
Disk Storage (> 200 GB)
  Access time: milliseconds

## Slide 41: Typical Memory Hierarchy
Microprocessor
Registers
L1 Cache
L2 Cache
Memory
Disk, Tape, etc
Memory Bus
I/O Bus
Faster
Bigger

## Slide 42: MAGNETIC DISK STORAGE
Track 0
Track 1
Sector
Recording area
Spindle
Direction of rotation
Platter
Read/write head
Actuator
Arm
Track 2

## Slide 43: MAGNETIC DISK STORAGE
Disk Access Time = Seek Time + Rotation Latency + Transfer Time
Seek Time: head movement to the desired track (milliseconds)
Rotation Latency: disk rotation until desired sector arrives under the head
Transfer Time: to transfer data

## Slide 44: Example on Disk Access Time
Given a magnetic disk with the following properties
  Rotation speed = 7200 RPM (rotations per minute)
  Average seek = 8 ms, Sector = 512 bytes, Track = 200 sectors
Calculate
  Time of one rotation (in milliseconds)
  Average time to access a block of 32 consecutive sectors

## Slide 45: Example on Disk Access Time
Given a magnetic disk with the following properties
  Rotation speed = 7200 RPM (rotations per minute)
  Average seek = 8 ms, Sector = 512 bytes, Track = 200 sectors
Calculate
  Time of one rotation (in milliseconds)
  Average time to access a block of 32 consecutive sectors
Answer
  Rotations per second
  Rotation time in milliseconds
  Average rotational latency
  Time to transfer 32 sectors
  Average access time
  = 7200/60 = 120 RPS
= 1000/120 = 8.33 ms
= time of half rotation = 4.17 ms
= (32/200) * 8.33 = 1.33 ms
= 8 + 4.17 + 1.33 = 13.5 ms